## Slide 1: With ULX3S
Presented by Miodrag Milanovic and Jan Dolinaj

## Slide 2: Who we are ?
Engineers
Hardware enthusiasts
Software developers
Very interested in FPGA
Working with Symbiotic EDA on NextPnR, Yosys, …

## Slide 3: ULX3S

## Slide 4: ULX3S - Top

## Slide 5: ULX3S-Bottom

## Slide 6: FPGA

## Slide 7: What is FPGA ?
Field-programmable gate array
Logic block – LUT + D Flip-Flop + full adder
I/O block – one per each pin
Interconnections, clock tree
Hard block – Block RAM, multipliers, DSP, CPU,…
Vendors: Xilinx, Intel/Altera, Lattice, Microsemi, Anlogic,
AGM, GoWin …

## Slide 8: Logic block
LUT
Full
Adder
MUX
MUX
MUX
D
Flip-Flop
Clock
Carry in
Carry out
Input
Output

## Slide 9: Lattice ECP5
Affordable price
From 12K to 85K
5G SERDES
Open source toolchain
Lot of nice boards available

## Slide 10: TOOLS

## Slide 11: How do we program FPGA ?
HDL - Hardware description language
VHDL and Verilog
Analysis: parsing and validation of HDL
Synthesis: HDL -> netlist
Place-and-route: netlist -> specific FPGA technology
Assembler: specific FPGA technology -> bitstream
Programming: deploying bitstream on device (serial flash memory or SRAM)
Timing analysis
Simulation

## Slide 12: Open source tools
Yosys - Verilog synthesis tool by Clifford Wolf
NextPnR - Place and route tool by Symbiotic EDA team
Project Trellis – Documenting the Lattice ECP5 bit-stream format by David Shah
APIO – micro-ecosystem for open FPGAs by Jesús Arroyo Torrens and Juan González (Obijuan)

## Slide 13: And more …
Arachne PnR - Place and route tool by Cotton Seed (ICE40)
Project IceStorm – Assembler, time analysis and FPGA programming tool by Clifford Wolf and Mathias Lasser (ICE40)
Icestudio - graphic editor for open FPGAs by Jesús Arroyo Torrens
Icarus Verilog by Stephen Williams
Verilator by Wilson Snyder with Duane Galbi and Paul Wasson
FuseSoC - package manager and a set of build tools for FPGA/ASIC development by Olof Kindgren

## Slide 14: YOSYS
This is a framework for RTL synthesis tools. It currently has extensive Verilog-2005 support and provides a basic set of synthesis algorithms for various application domains.
Yosys can be adapted to perform any synthesis job by combining the existing passes (algorithms) using synthesis scripts and adding additional passes as needed by extending the yosys C++ code base.
Yosys is free software licensed under the ISC license (a GPL compatible license that is similar in terms to the MIT license or the 2-clause BSD license).

## Slide 15: NextPnR
NextPnR aims to be a vendor neutral, timing driven, FOSS FPGA place and route tool.
Currently nextpnr supports:
Lattice iCE40 devices supported by Project IceStorm
Lattice ECP5 devices supported by Project Trellis
A "generic" back-end for user-defined architectures

## Slide 16: Project Trellis

## Slide 17: APIO
apio build
apio verify
apio lint
apio sim

## Slide 18: HANDS ON WORKSHOP

## Slide 19: Set up for your board
Enter tutorials folder of fpga-odysseus
apio init –board ulx3s-12f
If board is 1.7 revision :
cp ulx3s_v17patch.lpf ulx3s.lpf
All projects use symbolic links to these files

## Slide 20: BASICS

## Slide 21: Init
module top ( output wifi_gpio0 );
assign wifi_gpio0 = 1'b1;
endmodule
apio build
apio upload
apio clean

## Slide 22: LED
1
1
1
0
0
0
0
0

## Slide 23: Button
1
0
0
0
0
0
0
0

## Slide 24: Counter
reg [31:0] cnt = 0;
always @(posedge clk_25mhz)
begin
cnt <= cnt + 1;
end
assign led = cnt[31:24];

## Slide 25: Trigger
reg [7:0] cnt = 0;
always @(posedge btn[1])
begin
cnt <= cnt + 1;
end
assign led = cnt;
Button pressed

## Slide 26: Debounce

## Slide 27: AUDIO

## Slide 28: Theory
Digital – Analog Converter
PWM
We will change frequency of change, but keep 50% duty cycle

## Slide 29: Tone frequency

## Slide 30: Siren
parameter TONE_A4 = 25000000/440/2;
parameter TONE_A5 = 25000000/880/2;
always @(posedge clk_25mhz)
if(counter==26'b0)
begin
counter <= (tone[23] ? TONE_A4-1 : TONE_A5-1 );
audio_l <= ~audio_l;
audio_r <= ~audio_r;
end
else
counter <= counter-1;
A4 A4 A4
A5 A5 A5
A4 A4 A4
A5 A5 A5

## Slide 31: Piano
Button | Frequency
6 | 440 A4
5 | 494 B4
4 | 523 C5
3 | 587 D5
2 | 659 E5
1 | 698 F5

## Slide 32: PROTOCOLS

## Slide 33: FSM Finite State Machines

## Slide 34: Finite State Machines
Mealy Machine | Moore Machine
Output depends both upon the present state and the present input | Output depends only upon the present state.
Generally, it has fewer states than Moore Machine. | Generally, it has more states than Mealy Machine.
The value of the output function is a function of the transitions and the changes, when the input logic on the present state is done. | The value of the output function is a function of the current state and the changes at the clock edges, whenever state changes occur.
Mealy machines react faster to inputs. They generally react in the same clock cycle. | In Moore machines, more logic is required to decode the outputs resulting in more circuit delays. They generally react one clock cycle later.
Taken from www.tutorialspoint.com

## Slide 35: Serial protocol
Image taken from nandland.com

## Slide 36: Serial Transmit
data = 8'd65
cfg_divider = 25000000/115200
send_pattern <= {1'b1, data, 1'b0};
send_bitcnt <= 10;
send_divcnt <= 0;
send_pattern <= {1'b1, send_pattern[9:1]};
send_bitcnt <= send_bitcnt - 1;
send_divcnt <= 0;

## Slide 37: Serial connection
screen /dev/ttyUSB0 115200
Putty or anything similar

## Slide 38: Echo
PC
FPGA
RX
TX
Valid
Data
1
0
1
1
0
1

## Slide 39: SPI

## Slide 40: SPI data transfer

## Slide 41: VIDEO

## Slide 42: SPI Video
Visible area
64px
96 px
R | R | R | G | G | G | B | B

## Slide 43: VGA Video
Vertical front porch
Vertical back porch
Vertical sync
Horizontal front
porch
Horizontal
back
porch
Horizontal sync
Visible area

## Slide 44: HDMI

## Slide 45: Video block
spi_video video(
.clk(clk),
.oled_csn(oled_csn),
.oled_clk(oled_clk),
.oled_mosi(oled_mosi),
.oled_dc(oled_dc),
.oled_resn(oled_resn),
.x(x),
.y(y),
.color(color)
);
hdmi_video hdmi_video
(
.clk_25mhz(clk_25mhz),
.x(x),
.y(y),
.color(color),
.gpdi_dp(gpdi_dp),
.gpdi_dn(gpdi_dn)
);

## Slide 46: One color screen
assign color = 8'h02;
assign color = 24’h0000ff;

## Slide 47: Checkers
assign color = x[3] ^ y[3] ? 8'hff : 8'h00;
assign color = x[4] ^ y[4] ? 24'hffffff : 24'h000000;

## Slide 48: Tricolore
assign color = (x<32) ? 8'h02 : (x<64) ? 8'hff : 8'he0;
assign color = (x<213) ? 24'hff0000 : (x<426) ? 24'hffffff : 24'h0000ff;

## Slide 49: Text

## Slide 50: Text buffer
reg [7:0] mem [0:47];
integer k;
initial
begin
for (k = 0; k < 48; k = k + 1)
mem[k] <= 32;
mem[0] <= 8'd65;
mem[1] <= 8'd66;
mem[2] <= 8'd67;
end

## Slide 51: Terminal

## Slide 52: PONG

## Slide 53: Elements
Display
Paddle
Net
Ball
Score

## Slide 54: CPU

## Slide 55: Grom - 8
8 bit CPU​
1
4 general purpose registers​
2
12 bit address bus and PC (program counter)​
3
Code and data segment registers (CS,DS) (4 bit)​
4
Stack pointer (SP) (12 bit)​
5
8-bit ALU with C-carry, Z-zero and S-sign flags
6

## Slide 56: Instruction set (1/2)
IR |  |  | 2nd | Instruction | Info
0000 | dst | src |  | MOV dst, src | 
0001 | 00 | reg |  | ADD reg | r0 = r0 + reg
0001 | 01 | reg |  | SUB reg | r0 = r0 - reg
0001 | 10 | reg |  | ADC reg | r0 = r0 + reg + C
0001 | 11 | reg |  | SBC reg | r0 = r0 - reg - C
0010 | 00 | reg |  | AND reg | r0 = r0 and reg
0010 | 01 | reg |  | OR reg | r0 = r0 or reg
0010 | 10 | reg |  | NOT reg | r0 = not reg
0010 | 11 | reg |  | XOR reg | r0 = r0 xor reg
0011 | 00 | reg |  | INC reg | reg = reg + 1
0011 | 01 | reg |  | DEC reg | reg = reg - 1
0011 | 10 | reg |  | CMP reg | flags of r0 - reg
0011 | 11 | reg |  | TST reg | flags of r0 and reg
0100 | 00 | 00 |  | SHL | 
0100 | 00 | 01 |  | SHR | 
0100 | 00 | 10 |  | SAL | 
0100 | 00 | 11 |  | SAR | 
0100 | 01 | 00 |  | ROL | 
0100 | 01 | 01 |  | ROR | 
0100 | 01 | 10 |  | RCL | rotate with carry
0100 | 01 | 11 |  | RCR | rotate with carry
0100 | 10 | reg |  | PUSH reg | 
0100 | 11 | reg |  | POP reg | 
0101 | dst | src |  | LOAD dst, [src] | 
0110 | dst | src |  | STORE [dst], src | 
0111 | 00 | reg |  | MOV CS, reg | 
0111 | 01 | reg |  | MOV DS, reg | 
0111 | 10 | 00 |  | PUSH CS | 
0111 | 10 | 01 |  | PUSH DS | 
0111 | 10 | 10 |  | ??? | 
0111 | 10 | 11 |  | ??? | 
0111 | 11 | 00 |  | ??? | 
0111 | 11 | 01 |  | ??? | 
0111 | 11 | 10 |  | RET | 
0111 | 11 | 11 |  | HLT | 

## Slide 57: Instruction set (2/2)
1000 | 00 | 00 | val | JMP val | (unconditionally jump)
1000 | 00 | 01 | val | JC val | (carry=1 jump)
1000 | 00 | 10 | val | JNC val | (carry=0 jump)
1000 | 00 | 11 | val | JM val | (sign=1 jump)
1000 | 01 | 00 | val | JP val | (sign=0 jump)
1000 | 01 | 01 | val | JZ val | (zero=1 jump)
1000 | 01 | 10 | val | JNZ val | (zero=0 jump)
1000 | 01 | 11 | val | ??? | 
1000 | 10 | 00 | val | JR val | (unconditionally jump)
1000 | 10 | 01 | val | JRC val | (carry=1 jump)
1000 | 10 | 10 | val | JRNC val | (carry=0 jump)
1000 | 10 | 11 | val | JRM val | (sign=1 jump)
1000 | 11 | 00 | val | JRP val | (sign=0 jump)
1000 | 11 | 01 | val | JRZ val | (zero=1 jump)
1000 | 11 | 10 | val | JRNZ val | (zero=0 jump)
1000 | 11 | 11 | val | ??? | 
1001 | high |  | low | JUMP addr | 
1010 | high |  | low | CALL addr | 
1011 | high |  | low | MOV SP,addr | 
1100 | xx | reg | val | IN reg,[val] | 
1101 | xx | reg | val | OUT [val],reg | 
1110 | xx | 00 | val | MOV CS,val | 
1110 | xx | 01 | val | MOV DS,val | 
1110 | xx | 10 | val | ??? | 
1110 | xx | 11 | val | ??? | 
1111 | 00 | reg | val | MOV reg, val | 
1111 | 01 | reg | val | LOAD reg, [val] | 
1111 | 10 | reg | val | STORE [val], reg | 
1111 | 11 | xx |  | ??? | 

## Slide 58: ALU
ALU_OP_ADD :
tmp = A + B;
ALU_OP_SUB :
tmp = A - B;
ALU_OP_ADC :
tmp = A + B + { 7'b0000000, CF };
ALU_OP_SBC :
tmp = A - B - { 7'b0000000, CF };
ALU_OP_AND :
tmp = {1'b0, A & B };
ALU_OP_OR :
tmp = {1'b0, A | B };
ALU_OP_NOT :
tmp = {1'b0, ~B };
ALU_OP_XOR :
tmp = {1'b0, A ^ B};
ALU_OP_SHL :
tmp = { A[7], A[6:0], 1'b0};
ALU_OP_SHR :
tmp = { A[0], 1'b0, A[7:1]};
ALU_OP_SAL :
// Same as SHL
tmp = { A[7], A[6:0], 1'b0};
ALU_OP_SAR :
tmp = { A[0], A[7], A[7:1]};
ALU_OP_ROL :
tmp = { A[7], A[6:0], A[7]};
ALU_OP_ROR :
tmp = { A[0], A[0], A[7:1]};
ALU_OP_RCL :
tmp = { A[7], A[6:0], CF};
ALU_OP_RCR :
tmp = { A[0], CF, A[7:1]};

## Slide 60: Software running on our CPU
store[0] <= 8'b11100001; // MOV DS,2
store[1] <= 8'b00000010; //
store[2] <= 8'b01010100; // LOAD R1,[R0]
store[3] <= 8'b00110001; // INC R1
store[4] <= 8'b00110001; // INC R1
store[5] <= 8'b01100001; // STORE [R0],R1
store[6] <= 8'b11010001; // OUT [0],R1
store[7] <= 8'b00000000; //
store[8] <= 8'b00110001; // INC R1
store[9] <= 8'b10100001; // CALL 0x100
store[10] <= 8'b00000000; //
store[11] <= 8'b01111111; // HLT
store[256] <= 8'b11010001; // OUT [0],R1
store[257] <= 8'b00000000; //
store[258] <= 8'b01111110; // RET

## Slide 61: COMPUTER

## Slide 62: Altair
M – Memory examine and change
D – Dump memory
J – Jump to user program
J000000

## Slide 63: RISC-V

## Slide 64: Risc-V ISA
RV32I - Base Integer Instruction Set, 32-bit
RV64I - Base Integer Instruction Set, 64-bit
M - Standard Extension for Integer Multiplication and Division
C - Standard Extension for Compressed Instructions
A - Standard Extension for Atomic Instructions
F - Standard Extension for Single-Precision Floating-Point
D - Standard Extension for Double-Precision Floating-Point
Q - Standard Extension for Quad-Precision Floating-Point

## Slide 65: AttoSoC
PicoRV32
Memory
LEDs
Serial

## Slide 66: Building
make (to create firmware.hex)
apio build
apio upload
After change of files :
make clean
apio clean